ALLEGHANY COUNTY, VIRGINIA

BUILDING INSEPCTIONS DEPARTMENT

STRUCTURAL DRAWING CHECKLIST FOR

SINGLE FAMILY DWELLINGS

As of September 1, 2007, the Alleghany County Building Inspections Department will be requiring all applicants for new single-family dwellings to submit two sets of basic structural drawings for review prior to the issuance of a building permit.  One set will be returned to the contractor to keep at the job site.  Please answer “Yes” or “No” to the following questions. Any questions answered “No” will need to be addressed to and discussed the building department prior to the issuance of any permits.  At a minimum the following information shall be provided on the structural drawings submitted for approval:

|  | Item Descriptions | Yes | No |
| --- | --- | --- | --- |
| 1. | Dimensions of buildings and distance to property lines on site plan/sketch. |  |  |
| 2. | Wall section showing from the footings to the roof ridgeline that details the following: |  |  |
|  | A. Size of footings showing 18” frost line depth. |  |  |
|  | B. Trusses or rafters and joist with sizing and spans. |  |  |
|  | C. Wall framing. |  |  |
|  | D. Roof framing and coverings. |  |  |
|  | E. Insulations for floors, walls, and roof. |  |  |
| 3. | Floor plan that shows dimensions of rooms, whether finished or unfinished and the proposed use of the rooms. |  |  |
| 4. | Windows, size and safety glazing, if required. |  |  |
| 5. | Show all openings with header size or engineered member. |  |  |
| 6. | Stairways showing risers, treads, guards and rails. |  |  |
| 7. | Access and size of openings to attics and crawl spaces. |  |  |
| 8. | Ventilation in crawl spaces and attics. |  |  |
| 9. | If there is a garage attached to the dwelling, show fire ratings for walls, ceilings and structural members, if required. |  |  |
| 10. | Location of meter, electrical panels, and disconnects. |  |  |
| 11. | Location of smoke detectors, GFIC, and arc fault protected receptacles. |  |  |
| 12. | Type of HVAC systems and locations. |  |  |
| 13. | Exhaust systems for kitchens and bathrooms. |  |  |
| 14. | Location and type of any supplemental heating or cooling systems. |  |  |
| 15. | Furnish size and type of material to be used for water and wastewater lines |  |  |
| 16. | Treated lumber where required. |  |  |

If you have questions or need additional information regarding this check list or the building codes, please contact the Alleghany County Building Inspections Department at 540-863-6650 or in the Public Works Department of the Governmental Complex in Low Moor, 9212 Winterberry Avenue, Suite A, Covington, VA  24426.  If you wish to visit the office, it is strong suggested that you call ahead to make an appointment with the Building Official to ensure someone will be there to address your concerns.  The office hours are Monday through Friday 8:00 a.m. to 5:00 p.m.